## Slide 1: Introduction to cameras

## Slide 2: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Digital sensors

## Slide 3: Let’s design a camera
Idea 1: put a piece of film in front of an object
Do we get a reasonable image?
Slide by Steve Seitz

## Slide 4: Pinhole camera
Add a barrier to block off most of the rays
Slide by Steve Seitz
Notes: It gets inverted

## Slide 5: Pinhole camera

## Slide 6: Pinhole camera
Captures pencil of rays – all rays through a single point: aperture, center of projection, optical center, focal point, camera center, pinhole
The image is formed on the image plane
It is upside down (but that doesn’t matter)

## Slide 7: Accidental pinhole cameras are everywhere

## Slide 8: Accidental pinhole cameras are everywhere
Tree shadow during a solar eclipse
photo credit: Nils van der Burg http://www.physicstogo.org/index.cfm
Slide by Steve Seitz

## Slide 9: Camera obscura
Basic principle known to Mozi (470-390 BCE), Aristotle (384-322 BCE)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Source: A. Efros

## Slide 10: Turning a room into a camera obscura
Abelardo Morell, Camera Obscura Image of Manhattan View Looking South in Large Room, 1996
https://www.abelardomorell.net/camera-obscura
From Grand Images Through a Tiny Opening, Photo District News, February 2005

## Slide 11: Turning a room into a camera obscura
A. Torralba and W. Freeman, Accidental Pinhole and Pinspeck Cameras, CVPR 2012

## Slide 12: Modeling projection
How do we find the projection of a scene point ?
  Form the visual ray connecting to the camera center and find where it intersects the image plane
All scene points that lie on this visual ray have the same projection in the image
Are there scene points for which this projection is undefined?

## Slide 13: Modeling projection
Canonical coordinate system
  The optical center () is at the origin
  The z axis is the optical axis perpendicular to the image plane
  The xy plane is parallel to the image plane, x and y axes are horizontal and vertical directions of the image plane

## Slide 14: Abstraction with right handed coordinate system

## Slide 15: Deriving projected coordinates

## Slide 16: Deriving projected coordinates
Note: instead of dealing with an image that is upside down, most of the time we will pretend that the image plane is in front of the camera center

## Slide 17: Perspective effects

## Slide 18: Lines -> lines

## Slide 19: More distant objects are smaller

## Slide 20: Lines that are parallel in 3D meet in the image

## Slide 21: Lines that are parallel in 3D meet in the image

## Slide 22: Planes have horizons

## Slide 23: Planes have horizons

## Slide 24: On a plane, closer to horizon is further away

## Slide 25: Shapes are foreshortened

## Slide 26: Spot the property!
Piero della Francesca, Flagellation of Christ, 1455-1460

## Slide 27: Spot the property!
Piero della Francesca, Flagellation of Christ, 1455-1460

## Slide 28: Scaled orthographic projection

## Slide 29: Scaled orthographic projection

## Slide 30: Scaled orthographic projection in pictures of people
Likely SOP
Clearly perspective

## Slide 31: Why cameras have lenses
The pinhole is small, so relatively little light gets in (dark image)
Bigger pinhole -> brighter but fuzzier image
A lens system collects more light, but discourages fuzziness

## Slide 32: Home-made pinhole camera
What is wrong with this image?
Source: P. Debevec via A. Efros

## Slide 33: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction!
Slide by Steve Seitz

## Slide 34: Shrinking the aperture

## Slide 35: Overview
Pinhole projection model
Cameras with lenses

## Slide 36: Lens model – rotational symmetry
A lens focuses light onto the film
  Thin lens model:

## Slide 37: A thin lens, 2D drawing

## Slide 38: A thin lens, 2D drawing
Properties:
Ray arriving perp to lens plane passes through fp (I)
Ray arriving through fp leaves perp to lens (II)
Ray through lens center is unrefracted (III)
You can show: 1/f=1/w +1/d

## Slide 39: A thin lens, 2D drawing
Properties:
Previous slide identifies where rays leaving a world point focus
All other rays leaving world point and arriving at lens aperture focus on same point

## Slide 40: A thin lens – world point too close
Rays focus slightly behind image plane, constructing
a circle of confusion on image plane

## Slide 41: A thin lens – world point too far
Rays focus slightly in front of image plane, constructing
a circle of confusion on image plane

## Slide 42: The aperture of the lens
Bigger aperture -> bigger circle of confusion for point at fixed location

## Slide 43: The aperture of the lens
Smaller aperture -> Smaller circle of confusion for point at fixed location

## Slide 44: The aperture of the lens
Smaller aperture -> Smaller circle of confusion for point at fixed location
Bigger aperture -> bigger circle of confusion for point at fixed location
Alternatively:
Bigger aperture: collects more light but smaller depth of field
Smaller aperture: collects less light, but larger depth of field
Depth of field:
range of depths around focal plane where circle of confusion < threshold
(i.e. points in focus)

## Slide 45: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
Slide by Steve Seitz

## Slide 46: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
    All rays parallel to the optical axis pass through the focal point
    All parallel rays converge to points on the focal plane
Slide by Steve Seitz
focal point
f
focal plane

## Slide 47: Thin lens formula
Where does the lens focus the rays coming from a given point in the scene?
Slide by Frédo Durand
scene
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 48: Thin lens formula
What is the relation between the focal length ( f ), the distance of the object from the optical center (D), and the distance at which the object will be in focus (D′)?
f
D
D′
Slide by Frédo Durand
image plane
lens
scene
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 49: Thin lens formula
f
D
Similar triangles everywhere!
Slide by Frédo Durand
image plane
lens
D′
scene

## Slide 50: Thin lens formula
f
D
Similar triangles everywhere!
y′
y
y′/y = D′/D
Slide by Frédo Durand
image plane
lens
D′
scene

## Slide 51: Thin lens formula
f
D
Similar triangles everywhere!
y′
y
y′/y = (D′−f )/f
Slide by Frédo Durand
image plane
lens
y′/y = D′/D
D′
scene

## Slide 52: Thin lens formula
f
D
Any point satisfying the thin lens equation is in focus.
Slide by Frédo Durand
image plane
lens
What happens when D is very large?
D′
scene
Notes: And the set of all such points forms a plane parallel to the image (plane of focus).
Uses of the formula: given focal length and depth in scene that you want to be in focus, it tells you where to put the image plane. Given f and distance of image plane from camera center, it tells you which depth in the scene will be in focus.

## Slide 53: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view

## Slide 54: Depth of field
For a fixed focal length and image plane, there is a specific distance at which objects are “in focus”
  Other points project to a “circle of confusion” in the image

## Slide 55: Depth of field
Depth of field is the distance between the nearest and farthest objects in a scene that appear acceptably sharp in an image (Wikipedia)
Image source (via A. Efros)

## Slide 56: Controlling depth of field
Figure source

## Slide 57: Controlling depth of field
Figure source
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure

## Slide 58: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide by A. Efros

## Slide 59: Field of view
The field of view is the angular extent of the world observed by the camera (Wikipedia)
What determines the FOV?

## Slide 60: Field of view
The field of view is the angular extent of the world observed by the camera (Wikipedia)
What determines the FOV?
  Focal length (), length of the sensor ():
  Larger focal length = smaller FOV
f

## Slide 61: Field of view
Slide by A. Efros
Notes: The field of view is the angular extent of the world that is observed by the camera.

## Slide 62: Field of view
Slide by A. Efros

## Slide 63: Field of view / focal length
Large FOV, small f
Camera close to car
Small FOV, large f
Camera far from the car
Sources: A. Efros, F. Durand

## Slide 64: Same effect for faces
standard
wide-angle
telephoto
Source: F. Durand

## Slide 65: Approximating an orthographic camera
Source: Hartley & Zisserman

## Slide 66: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
http://en.wikipedia.org/wiki/Dolly_zoom

## Slide 67: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
“The Vertigo shot”
Example of dolly zoom from Goodfellas (YouTube)
Example of dolly zoom from La Haine (YouTube)

## Slide 68: My “dolly zoom”

## Slide 69: My “dolly zoom”

## Slide 70: Choice of lens and viewpoint: A COVID-era illustration
Source

## Slide 71: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations

## Slide 72: Real lenses

## Slide 73: Lens flaws: Vignetting

## Slide 74: Lens flaws: Radial distortion
No distortion
Pin cushion
Barrel
Caused by imperfect lenses
Distortion is stronger towards the edges of the photo

## Slide 75: Lens flaws: Spherical aberration
Spherical lenses don’t focus light perfectly
Rays farther from the optical axis focus closer

## Slide 76: Lens flaws: Chromatic aberration
Lens has different refractive indices for different wavelengths: causes color fringing
Near Lens Center
Near Lens Outer Edge

## Slide 77: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Digital sensors

## Slide 78: Digital camera sensors
Each cell in a sensor array is a light-sensitive diode that converts photons to electrons
  Dominant in the past: Charge Coupled Device (CCD)
  Dominant now: Complementary Metal Oxide Semiconductor (CMOS)
http://electronics360.globalspec.com/article/9464/ccd-vs-cmos-the-shift-in-image-sensor-technology

## Slide 79: Color filter arrays
Source: Steve Seitz
Demosaicing:
Estimation of missing components from neighboring values
Why more green?
Bayer grid (1976)
Human Luminance Sensitivity Function

## Slide 80: Color filter arrays
Demosaicing:
Estimation of missing components from neighboring values
Recent cameraphone technology: pixel binning
Bayer grid (1976)

## Slide 81: Camera response functions
Camera sensors are almost always linear BUT
image dynamic range is too big for 8 bits
Typical cameras apply a non-linearity before or during digitization – the camera response function
This varies from camera to camera

## Slide 82: Camera response functions

## Slide 83: Camera response functions – simulated images

## Slide 84: Misc. digital camera artifacts
Noise
    low light is where you most notice noise
    light sensitivity (ISO) / noise tradeoff
    stuck pixels
In-camera processing
    oversharpening can produce halos
Compression
    JPEG artifacts, blocking
Blooming
    CCD charge overflowing into neighboring pixels
Color artifacts
    Color moire
    Purple fringing from microlenses

## Slide 85: Historic milestones
Pinhole model: Mozi (470-390 BCE), Aristotle (384-322 BCE)
Principles of optics (including lenses): Alhacen (965-1039 CE)
Camera obscura: Leonardo da Vinci (1452-1519), Johann Zahn (1631-1707)
First photo: Joseph Nicephore Niepce (1822)
Daguerréotypes (1839)
Photographic film (Eastman, 1889)
Cinema (Lumière Brothers, 1895)
Color Photography (Lumière Brothers, 1908)
Television (Baird, Farnsworth, Zworykin, 1920s)
First consumer camera with CCD Sony Mavica (1981)
First fully digital camera: Kodak DCS100 (1990)
Niepce, “La Table Servie,” 1822
Alhacen’s notes
Old television camera
https://en.wikipedia.org/wiki/History_of_photography

## Slide 86: First digitally scanned photograph
NIST (1957), 176x176 pixels
http://listverse.com/history/top-10-incredible-early-firsts-in-photography/
Notes: From the website: “Russell Kirsch was a computer pioneer at the National Institute of Standards and Technology in the USA when he developed the system by which a camera could be fed into a computer. The photo is of Kirsch’s three month old son Walden and it measured a mere 176×176 pixels. Baby Walden now works in communications for Intel.”

## Slide 87: Camera sales over time
Source
Notes: CIPA: Camera & Imaging Products Association

## Slide 88: Camera sales over time
The full chart…
Source
Notes: CIPA: Camera & Imaging Products Association