## Slide 1: Image processing basics
Andy Warhol, Marilyn Diptych, 1962 (source)
Many slides adapted from Alyosha Efros, Derek Hoiem

## Slide 2: Image processing basics: Outline
Images as sampled functions
Sampling and reconstruction, aliasing
Image resampling, interpolation
Image transformations

## Slide 3: Model of imaging

## Slide 4: Image formation (preview)
What determines the brightness of an image pixel?
Light source(s)
Scene surface
Camera (lenses, shutter)
Image plane
Light energy arriving at per unit time is quantified by irradiance (Watts per sq. meter)
Strictly speaking, we need spectral irradiance to account for light across different wavelengths
Notes: Review slide (skip)

## Slide 7: Images as sampled functions

## Slide 8: Digital color image
R
G
B

## Slide 9
Why more green?
Human Luminance Sensitivity Function

## Slide 10: Cameras aren’t linear in input energy
This is deliberate,
and usually a property
of camera electronics.
Different cameras are
different
Helps imitate film
Increases dynamic range

## Slide 11: Images in Python
im = cv2.imread(filename) # read image
im = cv2.cvtColor(im, cv2.COLOR_BGR2RGB) # order channels as RGB
im = im / 255 # values range from 0 to 1
RGB image im is a H x W x 3 matrix (numpy.ndarray)
im[0,0,0] is the top-left pixel value in R-channel
im[y, x, c] is the value y+1 pixels down, x+1 pixels to right in the cth channel
im[H-1, W-1, 2] is the bottom-right pixel in B-channel
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column
How are the three color channels acquired?

## Slide 12: Acquiring 3 channels

## Slide 13: How are the three channels acquired?
Demosaicing:
Estimation of missing components from neighboring values
Why more green?
Bayer grid (1976)
Human Luminance Sensitivity Function
Source: Wikipedia
HOW? - shortly!

## Slide 14: Images as sampled functions
We like to think of a digital image as a sampled representation of a continuous function defined over a continuous 2D domain
Notes: Render with scanalyze????

## Slide 15: Sampling

## Slide 16: Image transformations
T
Upsampling

## Slide 17: Upsampling
Example:
go from 4x4 to 8x8
Forward warping: bad, do not do this
scan source, place pixels in target
issue: holes in target

## Slide 18: Upsampling
Example:
go from 4x4 to 8x8
Inverse warping:
scan target, for each pixel determine source value
usually, you must know the value at non-grid points

## Slide 19: Interpolation

## Slide 20: Interpolation
Nearest neighbors:

## Slide 21: Interpolation

## Slide 23: Interpolation
Bilinear Interpolation

## Slide 24: Bilinear interpolation more generally
http://en.wikipedia.org/wiki/Bilinear_interpolation
A
B
C
D

## Slide 26: Other kinds of interpolation
Source: Wikipedia

## Slide 28: Application: Demosaicing

## Slide 29: Image transformations
T
Downsampling

## Slide 30: Careless downsampling creates problems

## Slide 31: Aliasing “in the wild”
Source
Source
Source
Disintegrating textures
Moire patterns, false color

## Slide 32: Visualizing the problems

## Slide 33: Averaging before sampling can help

## Slide 34: Weighting the average can help

## Slide 35: Weighting the average can help, II

## Slide 36: Gaussian smoothing, I

## Slide 37: Gaussian smoothing, II

## Slide 38: Subsampling without pre-filtering
1/4 (2x zoom)
1/8 (4x zoom)
1/2
Source: S. Seitz (via D. Hoiem)

## Slide 39: Subsampling with pre-filtering
Image is smoothed with a Gaussian filter before subsampling
1/4
1/8
1/2
Source: S. Seitz (via D. Hoiem)

## Slide 40: Gaussian pyramids
Downsample x 4
smooth with big Gaussian, downsample x 4 (NO!)
OR
smooth, downsample x 2, smooth, downsample x 2
IDEA:
Pyramid: collection of smoothed and downsampled versions of an image

## Slide 41: Gaussian pyramid

## Slide 42: Gaussian pyramid
Notice that fine scale (hi res) version contains detail (mouse eye) and coarse scale (low res) shows large stuff (leaves)
Notice redundancy
coarse scale leaf predicts fine scale leaf.

## Slide 43: Laplacian pyramid
Notation for Gaussian pyramid ->
Idea:
reduce redundancy; instead of storing G_k, store
G_k-Upsample(G_{k+1})
Notice you can recover image
From either pyramid (Ex)

## Slide 44: Comparing

## Slide 45: Very simple processing with Laplacian pyramid
Reconstruction - all w = 1
Processing