## Slide 1: EKF-SLAM
D.A. Forsyth,
University of Illinois at Urbana Champaign

## Slide 2: Core idea
Observe the world from a moving platform
Build:
  a map of the world
  an estimate of pose in that map
Online:
  notice that new observations update:
    estimate of pose
    estimate of map
Filtering problem

## Slide 3: Some more details
With two cameras and some calibration:
  we can recover the position of 3D points
    in the vehicle’s coordinate system
      see triangulation movie, etc.
Together with an EKF, we can use this to recover
  points in world coordinates (a map)
  vehicle location
In fact, we can do all this with one camera
  with some minor care

## Slide 4: Big goal
Robot moving on the plane
  position, orientation
There are landmarks
  in fixed positions (for the moment….)
We start in some configuration
  (0, 0, 0)
  and move
Report posterior estimates of
  robot pos’n, orientation
  landmark positions in original coord frame
  when new landmarks appear, insert them
From Burgard et al slides

## Slide 5: Simple case
Vehicle is car, moves in 2D
Each measurement is
  a 2D measurement
  of position of a known beacon in vehicle coords
    (i.e. we know which measurement corresponds to which 3D point)

## Slide 6: Notation for dynamics

## Slide 7: Dynamics
Write
  s – speed along the midline
  r - rate of change of steering angle
Get:
Derivation at: https://msl.cs.uiuc.edu/planning/node658.html

## Slide 8: State
Position and orientation of the robot;
speed and rate of change of steering
All landmark positions
in original coordinate
frame
Landmark 1 position in OCF

## Slide 9: State update
The vehicle moves, as above;
  but the landmarks don’t move
  and there isn’t any noise

## Slide 10: Recall: The extended Kalman filter
Linearize:
Posterior covariance of x_{i-1}
Noise covariance

## Slide 11: Measuring position
Landmark is at:
  in world coordinate system
We record position in vehicle’s frame:
THIS ISN’T LINEAR!
vehicle posn in
world coords
point posn in
vehicle coords
point posn in
world coords
vehicle orientation
in world coords
Observation

## Slide 12: The steps, EKF:
Have:
Construct:
Now construct:
Where:
Measurement arrives:

## Slide 13: In principle, now easy
Rather horrid from the point of view of complexity
    looks like we have to invert a 3+2N by 3+2N matrix!
BUT
  F_x is much simpler than it might look
    the landmarks do not move!
  F_n ditto
    there is no noise in the landmark updates - the landmarks are fixed
  Outcome:
    We can deal with landmarks one by one
      and so do many small matrix inversions rather than one large one

## Slide 14: State update
The vehicle moves, as above;
  but the landmarks don’t move
  and there isn’t any noise

## Slide 15: State update, II
BUT
  F_x is much simpler than it might look
    the landmarks do not move!
  F_n ditto
    there is no noise in the landmark updates - the landmarks are fixed
3
2 N
N=Number of landmarks

## Slide 16: State update, III
Imagine we have 2 landmarks
Recall EKF:
Notice fewer matrix multiplies!

## Slide 17: State update, IV
Imagine we have 2 landmarks
Recall EKF:
Notice fewer matrix multiplies!

## Slide 18: More simplifications
BUT
  G_x is much simpler than it might look
    each set of measurements affected by only one landmark!
3
N
N=Number of landmarks
2
2 N

## Slide 19: More simplifications
BUT
  G_n is usually much simpler than it might look
    noise is usually additive normal noise
    This means that the term:
      is actually a block diagonal matrix

## Slide 20: Big simplification
The nasty bit…
But notice key point
  measurements interact only through the position/orientation of the vehicle
  each measurement depends on only one landmark and pose of v.
  OR measurements are conditionally independent conditioned on pose of v.
  OR you could subdivide time and update measurements one by one
  OR matrix G_x has the sparsity structure above
(the same point, manifesting in different ways)

## Slide 21: Subdividing time…
Receive observations in some order
  landmark i affects the whole state
    because it changes your estimate of the pose of the vehicle
      and that affects your estimate of state of every landmark
    BUT
      the change in estimate of pose depends ONLY on
        pose
        landmark i

## Slide 22: Subdividing time
Sequence
  repeat
    move (so make predictions)
    landmark 1 measurement arrives (update pose and so all based on 1)
    …
    landmark N measurement arrives (update pose and so all based on N)

## Slide 23
Steps in EKF

## Slide 24
Steps in EKF
One measurement from one landmark!
2 x 2
3+2N x 2
2 x 1
3+2Nx2
3+2Nx2
Notice:
Inverting only a small matrix
Notice:
But affecting the whole state!

## Slide 25: Landmarks
No measurement from a landmark?
  structure of EKF means you can process landmarks one by one
    that’s what all the matrix surgery was about
    so don’t update that landmark

## Slide 26: New landmarks
Sequence
  repeat
    move (so make predictions)
    landmark 1 measurement arrives (update pose and so all based on 1)
    …
    landmark N measurement arrives (update pose and so all based on N)
    check if there is a new landmark
      if so
        initialize landmark position and covariance
          conditioned on current state and measurement
        process from now on (we have N+1 landmarks)

## Slide 27: Variants
More complex vehicle dynamics
Different measurement process
  one camera
  LIDAR
  SONAR (v. hard)
  photo-consistency constraints (direct methods)
Multiple processes at different timescales
  fast:
    estimate configuration, landmarks
  slow:
    refine estimates (something like bundle adjustment)
    take more local image data into account

## Slide 28: Resources
Very nice collection of links at:
Challenging drone racing dataset at:
Drone racing team at:
Many cases at:
https://github.com/Taeyoung96/SLAM-Resources-for-Beginner?tab=readme-ov-file
https://fpv.ifi.uzh.ch
https://adr.utias.utoronto.ca
https://silenceoverflow.github.io/Awesome-SLAM/#LSurvey