## Slide 1: Image Intensity: Simple Physics
D.A. Forsyth
University of Illinois at Urbana Champaign

## Slide 2: Radiometry of image formation
What is the relationship between and ?
P
Radiance: energy carried by a ray
Measure of the density of photons traveling in a small cone of directions from towards
Power per unit area perpendicular to the direction of travel, per unit solid angle
Units: Watts per square meter per steradian
Irradiance: energy arriving at a surface
Incident power per unit area (not foreshortened)
Units: Watts per square meter

## Slide 3: Basic models of reflection
Specular reflection: light is reflected about the surface normal
Diffuse reflection: light scatters equally in all directions
incoming light
incoming light
Slide from D. Hoiem

## Slide 4: Diffuse and specular reflection

## Slide 5: Specular reflection
Radiation arriving along a source direction leaves along the specular direction (source direction reflected about normal)
Classic case: Mirror
Diagnosis
  When you look at a specular surface from different directions, appearance changes
  True specular surfaces are “really like” mirrors
    Form a clear image
Q:
  Why do mirrors reverse left and right, but not up and down?

## Slide 6: Specularities
On real surfaces, energy usually goes into a “lobe” of directions
  So image is blurred
  More usually, you see only the source
Specularities: narrow bright patches
  On metals: color of the metal
  Others: color of the light source

## Slide 7: Diffuse reflection
Light scatters equally in all directions
  E.g., brick, matte plastic, rough wood
Diagnosis:
  Surface has the same brightness when looked at from different directions
    (under fixed illumination)
Extremely common
  Very often surfaces are “largely” diffuse
Image source

## Slide 8: Orientation of diffuse surfaces

## Slide 9: Diffuse reflection: Lambert’s law
θ
(technically: radiosity, or total power leaving the surface per unit area)
: albedo (fraction of incident irradiance reflected by the surface)
: direction of light source (magnitude proportional to intensity of the source)
: unit surface normal
Notes: BRDF is constant
  Albedo: fraction of incident irradiance reflected by the surface
  Radiosity: total power leaving the surface per unit area (regardless of direction)

## Slide 10: Diffuse vs. specular: Significance
Same appearance
Totally different appearance
Diffuse
Specular
Source: J. Johnson and D. Fouhey
Same lighting, as close as possible camera settings, but different camera position

## Slide 11: Light at surface – other effects
Transparency
Refraction
Slide from D. Hoiem

## Slide 12
Subsurface scattering
Image source
Slide from D. Hoiem
Light at surface – other effects

## Slide 13
subsurface scattering in skin (not rendered!)

## Slide 14: Light at surface – other effects
Fluorescence
Phosphorescence
Image source
Slide from D. Hoiem
Notes: Fluorescence is light energy produced by a process where high-energy radiation (such as ultraviolet or X-ray) is absorbed by electrons surrounding an atom and is re-emitted as light energy. Unlike fluorescence, a phosphorescent material does not immediately re-emit the radiation it absorbs.
From https://www.pharmatutor.org/pharma-analysis/define-fluorescence-and-phosphorescence

## Slide 15: Fluorescence in nature
Many examples, mostly obscure:
scorpions, deep sea fish, teeth, nylon, chitons

## Slide 16: Films on surfaces
eg water
Assume:
  film is thin
You see:
  specular reflection+diffuse term

## Slide 17: Shadows

## Slide 18: Blurred shadows

## Slide 19: Area sources and their effects

## Slide 20: Dark shadows are rare indoors

## Slide 21: Interreflections
local shading model is poor
    because surfaces reflect light onto one another
Major nuisance;
  the distribution of light (in principle) depends on the configuration of every radiator;
  big distant ones are as important as small nearby ones (solid angle)
The effects are easy to model
It appears to be hard to extract information from these models

## Slide 22: Interreflections are a problem
but not a major one for photometric stereo – why?
From Koenderink slides on image texture and the flow of light

## Slide 23: Things to think about
Most people aren’t aware of colored interreflections
  even when you describe the physics
  WHY?
Why is it hard to use shadows as a shape cue?