## Slide 1: Camera calibration
Odilon Redon, Cyclops, 1914

## Slide 2: Overview
Camera calibration
  Intrinsic camera parameters
  Extrinsic camera parameters
  Estimation
First taste of 3D reconstruction: triangulation

## Slide 3: Perspective projection in normalized coordinates
Normalized (camera) coordinate system: camera center is at the origin, the principal axis is the -axis, and axes of the image plane are parallel to and axes of the world

## Slide 4: Perspective projection in normalized coordinates
Homogeneous coord. vec. of 3D point
Camera projection matrix
Homogeneous coord. vec. of image point
Equality up to scale

## Slide 5: Camera calibration: Overview
Camera calibration: figuring out transformation from world coordinate system to image coordinate system
world coordinate system
World to camera coord. trans. matrix (4x4)
Canonical projection matrix (3x4)
Camera to pixel coord. trans. matrix (3x3)
2D
point (3x1)
3D point (4x1)
Intrinsic camera parameters: principal point, scaling factors
Extrinsic camera parameters: rotation, translation

## Slide 6: Camera calibration: Overview
Camera calibration: figuring out transformation from world coordinate system to image coordinate system
world coordinate system
World to camera coord. trans. matrix (4x4)
Canonical projection matrix (3x4)
Camera to pixel coord. trans. matrix (3x3)
2D
point (3x1)
3D point (4x1)
General camera projection matrix

## Slide 7: Intrinsic parameters: Principal point
Principal point (): point where principal axis intersects the image plane
In the normalized coordinate system, the origin of the image is at the principal point, or camera center
In the image coordinate system: the origin is in the corner

## Slide 8: Intrinsic parameters: Principal point
We want the principal point to map to instead of
px
py

## Slide 9: Intrinsic parameters: Principal point
calibration matrix
Principal point:
py
Canonical projection matrix
px

## Slide 10: Intrinsic parameters: Principal point
calibration matrix
Canonical projection matrix
What are the units of the focal length and principal point coordinates ?
  Same as world units – presumably metric units
What units do we want for measuring image coordinates?
  Pixel units
Thus, we need to introduce scaling factors for mapping from world to pixel units

## Slide 11: Intrinsic parameters: Scaling factors
pixels/m in horizontal direction, pixels/m in vertical direction
Pixel size (m):
pixels/m
m
pixels
Camera sensor
Calibration matrix in metric units
Scaling factors
Calibration matrix in pixel units
Notes: To convert from metric image coordinates to pixel coordinates, we have to multiply the x, y coordinates by the x, y pixel magnification factors (pix/m)
Beta_x, beta_y is the principal point coordinates in pixels

## Slide 12: Extrinsic parameters: Rotation and translation
In general, the camera coordinate frame will be related to the world coordinate frame by a rotation and a translation
camera coordinate system
world coordinate system

## Slide 13: Extrinsic parameters: Rotation and translation
In general, the camera coordinate frame will be related to the world coordinate frame by a rotation and a translation
coords. of point in normalized camera frame
coords. of camera center in world frame
coords. of a point in world frame
In non-homogeneous coordinates, the transformation from world to normalized camera coordinate system is given by:
camera coordinate system
world coordinate system
3x3 rotation matrix

## Slide 14: Extrinsic parameters: Rotation and translation
3D transformation matrix (4 x 4)
In non-homogeneous coordinates:
In homogeneous coordinates:

## Slide 15: Extrinsic parameters: Rotation and translation
In non-homogeneous coordinates:
In homogeneous coordinates:
3D transformation matrix (4 x 4)

## Slide 16: Extrinsic parameters: Rotation and translation
In non-homogeneous coordinates:
In homogeneous coordinates:
Transformation from normalized 3D coordinates to pixel image coordinates:

## Slide 17: Extrinsic parameters: Rotation and translation
In homogeneous coordinates:
Finally:

## Slide 18: Extrinsic parameters: Rotation and translation
The focal point is the null space of the projection matrix!
What is the projection of the focal point in world coordinates?
coords. of camera center in world frame

## Slide 19: Camera parameters: Summary
Intrinsic parameters
  Principal point coordinates
  Focal length
  Pixel magnification factors
  Skew (non-rectangular pixels) – tends to get ignored in practice
  Radial distortion – important in practice!

## Slide 20: Camera extrinsics
Rotation matrix - orthornormal, det=1
Extrinsics
Intrinsics

## Slide 21: Camera intrinsics
Extrinsics
Intrinsics

## Slide 22: Overview
Camera calibration
  Intrinsic camera parameters
  Extrinsic camera parameters
  Estimation

## Slide 23: Camera calibration

## Slide 24: Camera calibration
Given points with known 3D coordinates and known image projections , estimate the camera parameters

## Slide 25: Camera calibration
Given points with known 3D coordinates and known image projections , estimate the camera parameters
312.747 309.140 30.086
305.796 311.649 30.356
307.694 312.358 30.418
310.149 307.186 29.298
311.937 310.105 29.216
311.202 307.572 30.682
307.106 306.876 28.660
309.317 312.490 30.230
307.435 310.151 29.318
308.253 306.300 28.881
306.650 309.301 28.905
308.069 306.831 29.189
309.671 308.834 29.029
308.255 309.955 29.267
307.546 308.613 28.963
311.036 309.206 28.913
307.518 308.175 29.069
309.950 311.262 29.990
312.160 310.772 29.080
311.988 312.709 30.514
880 214
43 203
270 197
886 347
745 302
943 128
476 590
419 214
317 335
783 521
235 427
665 429
655 362
427 333
412 415
746 351
434 415
525 234
716 308
602 187
Image credit: J. Hays
Known 2D image coords
Known 3D locations

## Slide 26: Camera calibration: non-linear method
N reference points with known position in 3D
Predict the locations of the known points in camera using
estimated camera parameters
Compare to observed locations
Minimize least-squares error

## Slide 27: Camera calibration: non-linear method
Two issues:
write out equations for optimization problem
good start point for optimization

## Slide 28: Camera extrinsics
Rotation matrix - orthornormal, det=1
Extrinsics
Intrinsics

## Slide 29: Camera intrinsics
Extrinsics
Intrinsics

## Slide 30: Camera calibration: non-linear, equations
The i’s are intrinsic parameters
(remember, this is upper triangular)
The e’s are extrinsic parameters
(they are constrained)

## Slide 31: Camera calibration: non-linear
Strategy:
chuck it into a constrained optimizer and run
this fails – you need a good starting point
Start point:
neat linear construction

## Slide 32: Camera calibration: Linear method
One match gives two linearly independent constraints on the camera matrix
x component of location of i’th point in image

## Slide 33: Calibration: Linear method
N points gives 2N homogeneous equations
The camera matrix is 3 x 4 but scale doesn’t matter so there are
11 degrees of freedom – we can estimate it with 6 points

## Slide 34: Camera calibration: Linear method
Recall homography fitting:
One match gives two linearly independent constraints

## Slide 35: Camera calibration: Linear method
Final linear system:
One 2D/3D correspondence gives two linearly independent equations
  The projection matrix has 11 degrees of freedom
  6 correspondences needed for a minimal solution
Homogeneous least squares: find minimizing
  Solution is eigenvector of corresponding to smallest eigenvalue

## Slide 36: Camera calibration: Linear method
Final linear system:
What if all the 3D points are coplanar, i.e., there exists a set of line parameters such that for all ?
  Then we will get degenerate solutions , , or

## Slide 37: Camera parameters from camera matrix
Camera matrix is:

## Slide 38: Camera parameters from camera matrix
Camera matrix is:

## Slide 39: Parameters from camera matrix

## Slide 40: Parameters from camera matrix

## Slide 41: Camera calibration: nonlinear
non-linear methods are preferred
  Can include radial distortion and constraints such as known focal length, orthogonality, visibility of points

## Slide 42: Camera calibration using vanishing points
If world coordinates of reference 3D points are not known, in special cases, we may be able to use vanishing points
Source: A. Efros, A. Criminisi

## Slide 43: Camera calibration using vanishing points
If world coordinates of reference 3D points are not known, in special cases, we may be able to use vanishing points
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
Source: A. Efros, A. Criminisi

## Slide 44: Review: Vanishing points
image plane
line in the scene
vanishing point
All lines having the same direction share the same vanishing point
camera
center

## Slide 45: Computing vanishing points
is a point at infinity, is its projection:
Let’s parameterize the line using point and direction vector :

## Slide 46: Calibration from vanishing points
Consider a scene with three orthogonal vanishing directions:
Note: , are finite vanishing points and is an infinite vanishing point
.
.
Notes: The third homogeneous coordinate of an infinite vanishing point is 0. Infinite vanishing points correspond to directions of lines that are parallel to the image plane.

## Slide 47: Calibration from vanishing points
Consider a scene with three orthogonal vanishing directions:
We can align the world coordinate system with these directions
.
.

## Slide 48: Projection of the world coordinate system

## Slide 49: Projection of the world coordinate system

## Slide 50: Projection of the world coordinate system

## Slide 51: Projection of the world coordinate system
Vanishing points in , , directions
(i.e., , , )

## Slide 52: Projection of the world coordinate system
Projection of world origin
Problem: this only gives us the four columns up to independent scale factors, additional constraints needed to solve for them
Vanishing points in , , directions
(i.e., , , )

## Slide 53: Calibration from vanishing points
Let us align the world coordinate system with three orthogonal vanishing directions in the scene:

## Slide 54: Calibration from vanishing points
Let us align the world coordinate system with three orthogonal vanishing directions in the scene:
Orthogonality constraint:

## Slide 55: Calibration from vanishing points
Let us align the world coordinate system with three orthogonal vanishing directions in the scene:
Orthogonality constraint:
Extrinsic parameter matrix () disappears and we are left with constraints on the calibration matrix!

## Slide 56: Calibration from vanishing points
How many constraints do we get?
  Three: one for each pair of vanishing points
How many unknown parameters does have?
  Three:
A couple of complications:
  The constraints are nonlinear, but it’s not hard to do the algebra (omitted)
  At least two finite vanishing points are needed to solve for both focal length and principal point

## Slide 57: Calibration from vanishing points
Can solve for focal length, principal point
Cannot recover focal length, principal point is the third vanishing point

## Slide 58: Rotation from vanishing points
Constraints on vanishing points:
We just used orthogonality constraints to solve for
Now we have:
Notice:
Thus,
The scale ambiguity goes away since we require

## Slide 59: Calibration from vanishing points: Summary
Solve for intrinsic parameters (focal length, principal point) using three orthogonal vanishing points
Get extrinsic parameters (rotation) directly from vanishing points once calibration matrix is known
Advantages
  No need for calibration chart, 2D-3D correspondences
  Could be completely automatic
Disadvantages
  Only applies to certain kinds of scenes
  It is tricky to accurately localize vanishing points
  Need at least two finite vanishing points

## Slide 60: Overview
Camera calibration
  Intrinsic camera parameters
  Extrinsic camera parameters
  Estimation
First taste of 3D reconstruction: triangulation

## Slide 61: Triangulation
Given projections of a 3D point in two or more images (with known camera matrices), find the coordinates of the point

## Slide 62: Triangulation
Given projections of a 3D point in two or more images (with known camera matrices), find the coordinates of the point

## Slide 63: Triangulation
Given projections of a 3D point in two or more images (with known camera matrices), find the coordinates of the point

## Slide 64: Triangulation
We want to intersect the two visual rays corresponding to and , but because of noise and numerical errors, they don’t meet exactly

## Slide 65: Triangulation: Geometric approach
Find shortest segment connecting the two viewing rays and let be the midpoint of that segment

## Slide 66: Triangulation: Nonlinear approach
Find that minimizes

## Slide 67: Triangulation: Linear approach
Rewrite cross product as matrix multiplication:

## Slide 68: Triangulation: Linear approach
Two independent equations each in terms of three unknown entries of

## Slide 69: Preview: Structure from motion
Camera 3
Figure credit: Noah Snavely
Camera 1
Camera 2
Given 2D point correspondences between multiple images, compute the camera parameters and the 3D points
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 70: Preview: Structure from motion
Camera 3
Camera 1
Camera 2
Structure: Given known cameras and projections of the same 3D point in two or more images, compute the 3D coordinates of that point
  Triangulation!
?
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 71: Preview: Structure from motion
Camera 3
Camera 1
Camera 2
Motion: Given a set of known 3D points seen by a camera, compute the camera parameters
  Calibration!
?
?
?
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 72: Multi-view geometry “Bible”