## Slide 1: Obtaining Images
D.A. Forsyth,
University of Illinois at Urbana Champaign
Some slides adapted from
Svetlana Lazebnik, who adapted from Alyosha Efros, Derek Hoiem

## Slide 2: Model of imaging

## Slide 3: A Pinhole Camera

## Slide 4: The Pinhole Camera

## Slide 6: Image formation (preview)
What determines the brightness of an image pixel?
Light source(s)
Scene surface
Camera (lenses, shutter)
Image plane
Light energy arriving at per unit time is quantified by irradiance (Watts per sq. meter)
Strictly speaking, we need spectral irradiance to account for light across different wavelengths
Notes: Review slide (skip)

## Slide 9: Cameras aren’t linear in input energy
This is deliberate, and usually a property of camera electronics.
  Helps imitate film
  Increases dynamic range
It’s not the sensor (which is usually linear)
  you can usually get linear pix from cameras with enough work
Different cameras have different nonlinearities

## Slide 10
From wikipedia, https://commons.wikimedia.org/wiki/File:Raw_vs_jpg.jpg

## Slide 11
https://commons.wikimedia.org/wiki/File:Raw_vs_jpg.jpg

## Slide 12
https://commons.wikimedia.org/wiki/File:Raw_vs_jpg.jpg

## Slide 13: Images as sampled functions

## Slide 14: Digital color image
R
G
B

## Slide 15
Why more green?
Human Luminance Sensitivity Function

## Slide 16: Images in Python
im = cv2.imread(filename) # read image
im = cv2.cvtColor(im, cv2.COLOR_BGR2RGB) # order channels as RGB
im = im / 255 # values range from 0 to 1
RGB image im is a H x W x 3 matrix (numpy.ndarray)
im[0,0,0] is the top-left pixel value in R-channel
im[y, x, c] is the value y+1 pixels down, x+1 pixels to right in the cth channel
im[H-1, W-1, 2] is the bottom-right pixel in B-channel
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column

## Slide 17: Pointwise image transformations
Apply the same function to each pixel value
  perhaps different for R, G, B
Simple applications
  remove camera non-linearity
  simulate different camera
  increase/reduce contrast

## Slide 19: Other sensors...
Basically, light cameras with extra tricks
  IR cameras
    light cameras at different wavelengths
      but you might have to cool sensors
  Polarization cameras
    specialized sensors to measure intensity at particular polarizations
  Multispectral cameras
    various arrangements to image with more sensors than R, G, and B
Really different
  Depth cameras

## Slide 20: Two cameras yield depth

## Slide 22: If’s, and’s and but’s...

## Slide 24: Camera – projector stereo

## Slide 25: Structured light

## Slide 26: LIDAR