## Slide 1: Introduction to cameras

## Slide 2: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Digital sensors

## Slide 3: Let’s design a camera
Idea 1: put a piece of film in front of an object
Do we get a reasonable image?
Slide by Steve Seitz

## Slide 4: Pinhole camera
Add a barrier to block off most of the rays
Slide by Steve Seitz
Notes: It gets inverted

## Slide 5: Pinhole camera
Captures pencil of rays – all rays through a single point: aperture, center of projection, optical center, focal point, camera center
The image is formed on the image plane
Slide by Steve Seitz

## Slide 6: Pinhole cameras are everywhere

## Slide 7: Pinhole cameras are everywhere
Tree shadow during a solar eclipse
photo credit: Nils van der Burg http://www.physicstogo.org/index.cfm
Slide by Steve Seitz

## Slide 8: Camera obscura
Basic principle known to Mozi (470-390 BCE), Aristotle (384-322 BCE)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Source: A. Efros

## Slide 9: Turning a room into a camera obscura
Abelardo Morell, Camera Obscura Image of Manhattan View Looking South in Large Room, 1996
https://www.abelardomorell.net/camera-obscura
From Grand Images Through a Tiny Opening, Photo District News, February 2005

## Slide 10: Turning a room into a camera obscura
A. Torralba and W. Freeman, Accidental Pinhole and Pinspeck Cameras, CVPR 2012

## Slide 11: Modeling projection
How do we find the projection of a scene point ?
  Form the visual ray connecting to the camera center and find where it intersects the image plane
All scene points that lie on this visual ray have the same projection in the image
Are there scene points for which this projection is undefined?

## Slide 12: Modeling projection
Canonical coordinate system
  The optical center () is at the origin
  The z axis is the optical axis perpendicular to the image plane
  The xy plane is parallel to the image plane, x and y axes are horizontal and vertical directions of the image plane

## Slide 13: Deriving projected coordinates

## Slide 14: Deriving projected coordinates
Note: instead of dealing with an image that is upside down, most of the time we will pretend that the image plane is in front of the camera center

## Slide 15: Properties of projection
Real-world sizes (lengths) are not preserved in projection
  What other properties are/are not preserved?
Piero della Francesca, Flagellation of Christ, 1455-1460

## Slide 16: Home-made pinhole camera
What is wrong with this image?
Source: P. Debevec via A. Efros

## Slide 17: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction!
Slide by Steve Seitz

## Slide 18: Shrinking the aperture

## Slide 19: Overview
Pinhole projection model
Cameras with lenses

## Slide 20: Adding a lens
Slide by Steve Seitz
A lens focuses light onto the film
  Thin lens model:

## Slide 21: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
Slide by Steve Seitz

## Slide 22: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
    All rays parallel to the optical axis pass through the focal point
    All parallel rays converge to points on the focal plane
Slide by Steve Seitz
focal point
f
focal plane

## Slide 23: Thin lens formula
Where does the lens focus the rays coming from a given point in the scene?
Slide by Frédo Durand
scene
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 24: Thin lens formula
What is the relation between the focal length ( f ), the distance of the object from the optical center (D), and the distance at which the object will be in focus (D′)?
f
D
D′
Slide by Frédo Durand
image plane
lens
scene
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 25: Thin lens formula
f
D
Similar triangles everywhere!
Slide by Frédo Durand
image plane
lens
D′
scene

## Slide 26: Thin lens formula
f
D
Similar triangles everywhere!
y′
y
y′/y = D′/D
Slide by Frédo Durand
image plane
lens
D′
scene

## Slide 27: Thin lens formula
f
D
Similar triangles everywhere!
y′
y
y′/y = (D′−f )/f
Slide by Frédo Durand
image plane
lens
y′/y = D′/D
D′
scene

## Slide 28: Thin lens formula
f
D
Any point satisfying the thin lens equation is in focus.
Slide by Frédo Durand
image plane
lens
What happens when D is very large?
D′
scene
Notes: And the set of all such points forms a plane parallel to the image (plane of focus).
Uses of the formula: given focal length and depth in scene that you want to be in focus, it tells you where to put the image plane. Given f and distance of image plane from camera center, it tells you which depth in the scene will be in focus.

## Slide 29: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view

## Slide 30: Depth of field
For a fixed focal length and image plane, there is a specific distance at which objects are “in focus”
  Other points project to a “circle of confusion” in the image

## Slide 31: Depth of field
Depth of field is the distance between the nearest and farthest objects in a scene that appear acceptably sharp in an image (Wikipedia)
Image source (via A. Efros)

## Slide 32: Controlling depth of field
Figure source

## Slide 33: Controlling depth of field
Figure source
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure

## Slide 34: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide by A. Efros

## Slide 35: Field of view
The field of view is the angular extent of the world observed by the camera (Wikipedia)
What determines the FOV?

## Slide 36: Field of view
The field of view is the angular extent of the world observed by the camera (Wikipedia)
What determines the FOV?
  Focal length (), length of the sensor ():
  Larger focal length = smaller FOV
f

## Slide 37: Field of view
Slide by A. Efros
Notes: The field of view is the angular extent of the world that is observed by the camera.

## Slide 38: Field of view
Slide by A. Efros

## Slide 39: Field of view / focal length
Large FOV, small f
Camera close to car
Small FOV, large f
Camera far from the car
Sources: A. Efros, F. Durand

## Slide 40: Same effect for faces
standard
wide-angle
telephoto
Source: F. Durand

## Slide 41: Approximating an orthographic camera
Source: Hartley & Zisserman

## Slide 42: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
http://en.wikipedia.org/wiki/Dolly_zoom

## Slide 43: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
“The Vertigo shot”
Example of dolly zoom from Goodfellas (YouTube)
Example of dolly zoom from La Haine (YouTube)

## Slide 44: My “dolly zoom”

## Slide 45: My “dolly zoom”

## Slide 46: Choice of lens and viewpoint: A COVID-era illustration
Source

## Slide 47: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations

## Slide 48: Real lenses

## Slide 49: Lens flaws: Vignetting

## Slide 50: Lens flaws: Radial distortion
No distortion
Pin cushion
Barrel
Caused by imperfect lenses
Distortion is stronger towards the edges of the photo

## Slide 51: Lens flaws: Spherical aberration
Spherical lenses don’t focus light perfectly
Rays farther from the optical axis focus closer

## Slide 52: Lens flaws: Chromatic aberration
Lens has different refractive indices for different wavelengths: causes color fringing
Near Lens Center
Near Lens Outer Edge

## Slide 53: Overview
Pinhole projection model
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Digital sensors

## Slide 54: Digital camera sensors
Each cell in a sensor array is a light-sensitive diode that converts photons to electrons
  Dominant in the past: Charge Coupled Device (CCD)
  Dominant now: Complementary Metal Oxide Semiconductor (CMOS)
http://electronics360.globalspec.com/article/9464/ccd-vs-cmos-the-shift-in-image-sensor-technology

## Slide 55: Color filter arrays
Source: Steve Seitz
Demosaicing:
Estimation of missing components from neighboring values
Why more green?
Bayer grid (1976)
Human Luminance Sensitivity Function

## Slide 56: Color filter arrays
Demosaicing:
Estimation of missing components from neighboring values
Recent cameraphone technology: pixel binning
Bayer grid (1976)

## Slide 57: Misc. digital camera artifacts
Noise
    low light is where you most notice noise
    light sensitivity (ISO) / noise tradeoff
    stuck pixels
In-camera processing
    oversharpening can produce halos
Compression
    JPEG artifacts, blocking
Blooming
    CCD charge overflowing into neighboring pixels
Color artifacts
    Color moire
    Purple fringing from microlenses

## Slide 58: Historic milestones
Pinhole model: Mozi (470-390 BCE), Aristotle (384-322 BCE)
Principles of optics (including lenses): Alhacen (965-1039 CE)
Camera obscura: Leonardo da Vinci (1452-1519), Johann Zahn (1631-1707)
First photo: Joseph Nicephore Niepce (1822)
Daguerréotypes (1839)
Photographic film (Eastman, 1889)
Cinema (Lumière Brothers, 1895)
Color Photography (Lumière Brothers, 1908)
Television (Baird, Farnsworth, Zworykin, 1920s)
First consumer camera with CCD Sony Mavica (1981)
First fully digital camera: Kodak DCS100 (1990)
Niepce, “La Table Servie,” 1822
Alhacen’s notes
Old television camera
https://en.wikipedia.org/wiki/History_of_photography

## Slide 59: First digitally scanned photograph
NIST (1957), 176x176 pixels
http://listverse.com/history/top-10-incredible-early-firsts-in-photography/
Notes: From the website: “Russell Kirsch was a computer pioneer at the National Institute of Standards and Technology in the USA when he developed the system by which a camera could be fed into a computer. The photo is of Kirsch’s three month old son Walden and it measured a mere 176×176 pixels. Baby Walden now works in communications for Intel.”

## Slide 60: Camera sales over time
Source
Notes: CIPA: Camera & Imaging Products Association

## Slide 61: Camera sales over time
The full chart…
Source
Notes: CIPA: Camera & Imaging Products Association