## Slide 1: The Weather
D.A. Forsyth, UIUC

## Slide 2: Key points
Weather effects cause detectors to work poorly
  We can collect weathered data
  OR unweather using regression procedures
  OR we can train on artificially weathered data

## Slide 3: How weather affects images

## Slide 4: Scattering
Fundamental mechanism of light/matter interactions
Visually important for
  slightly translucent materials (skin, milk, marble, etc.)
  participating media

## Slide 5: Participating media
for example,
  smoke,
  wet air (mist, fog)
  rain
  dusty air
  air at long scales
Light leaves/enters a ray travelling through space
  leaves because it is scattered out
  enters because it is scattered in
New visual effects

## Slide 6: Light hits a small box of material

## Slide 7: A ray passing through scattering material

## Slide 8: Airlight as a scattering effect

## Slide 9: Absorption
Ignore in-scattering
  only account for forward scattering
Assume there is a source at t=T
  of intensity I(T)
  what do we see at t=0?
Eye ray
Box of material
Eye ray
dt
Want I(0)
(at start of eye ray)
t

## Slide 10
Cross sectional area of “slab” is E
Contains particles, radius r, density rho
Too few to overlap when projected
% light absorbed = (area of projected particles)/
(area of slab)
This is:
Eye is at 0
Intensity at T

## Slide 11
From Lynch and Livingstone, Color and Light in Nature

## Slide 13: This sort of thing affects detectors, etc.
Fairly clear (more later)
What to do:
  Train detectors on real weather images
    hard - collect and mark them up; rich collection of effects
    mostly, this won’t work out
  Remove weather effects, then apply detector
    Q: Remove how?
      Simple physics
      Regression (next)
  Take training images, synthesize weather on top
    Q: How?
      complicated mixture of physics and advanced regression tricks

## Slide 14: Paired data
Collect data on good days, bad days
  along the same routes, w/ GPS
  use dynamic programming, GPS to compute alignment at the image level
Now label
  annotator labels bad image round 1
  compares to good image; fixes labelling round 2
Sakaridis et al, 21

## Slide 15: Weather and Speculation
0: Why
I: Weather
  simple physics of fog;
II: Image regression
  images from images, using training data
II: Weather, more
  what to do? correct, or train on weather data; either requires simulation
III: Speculation
  the idea of image generation; adversaries
  fun with styleGAN -II relighting
  extreme case: NERFY representations and weather NERF

## Slide 16: Fog and airlight

## Slide 17: This sort of thing affects detectors, etc.
Fairly clear (more later)
What to do:
  Train detectors on real weather images
    hard - collect and mark them up; rich collection of effects
    mostly, this won’t work out
  Remove weather effects, then apply detector
    Q: Remove how?
      Simple physics
      Regression (next)
  Take training images, synthesize weather on top
    Q: How?
      complicated mixture of physics and advanced regression tricks

## Slide 18: Removing haze by physical reasoning
Consequences
  Brightness is a depth cue
  Reasoning about airlight color yields dehazed image
Image color at p
Surface radiance color at p
Absorption term, exponential in depth, at p
Airlight color at p

## Slide 19: Airlight yields a depth cue
Assume that airlight is dominant
  (i.e. most of light arriving at camera is airlight)
  then you can recover depth from a single image
Disadvantages
  requires significant fog (but not too much) or large scales

## Slide 20
Nayar and Narasimhan, 1999

## Slide 21: Model
With work, this yields
  neighboring pixels with same albedo yield
    constraints on shading and T
  assume shading and T independent
    estimate A to yield “most independent” shading and T
  result: J(p)
Observed
Shading x albedo
Independent of shading
Airlight color - same at all points

## Slide 22
Fattal, 08 - note depth map AND dehaze; note also slightly odd colors

## Slide 23
Improved estimation by cleaner model
Fattal, 08 - note depth map AND dehaze; note also slightly odd colors

## Slide 24: This sort of thing affects detectors, etc.
Fairly clear (more later)
What to do:
  Train detectors on real weather images
    hard - collect and mark them up; rich collection of effects
    mostly, this won’t work out
  Remove weather effects, then apply detector
    Q: Remove how?
      Simple physics
      Regression
  Take training images, synthesize weather on top
    Q: How?
      complicated mixture of physics and advanced regression tricks

## Slide 25: Image regression
Take an image, predict something “like” an image
  Underlying technology is straightforward, significant tricks
Cases
  train with real paired data eg (image, foggy version of image)
  train with fake paired data eg (image, simulated foggy version of image)
  train with unpaired data; important, we’ll ignore
Motivating problems
  image -> depth
    also, image pair -> optic flow; low res image-> high res image
  image -> foggy image; image -> rainy image
Mechanics sketched yesterday

## Slide 26: Paired datasets
Obtain pairs (hazy image, clear image)
Real data:
  Take photos outdoors; introduce fog; repeat
    NH-HAZE
      https://data.vision.ee.ethz.ch/cvl/ntire20/nh-haze/
Synthesized data:
  Fake fog model on real image
    Foggy cityscapes
      https://people.ee.ethz.ch/~csakarid/SFSU_synthetic/
  Render synthetic images fog/no-fog
    RESIDE
      https://arxiv.org/pdf/1712.04143.pdf

## Slide 27
Cai et al 16 (DeHazeNet)

## Slide 28: Single image dehazing
Shen et al 19

## Slide 29
Qin et al 19 - Use feature attention

## Slide 30: Side topic - Adversarial losses
Issue:
  we are making pictures that should have a strong structure
    eg - it should be “like” a true image
    but we don’t know how to write a loss that imposes that structure
Strategy:
  build a classifier that tries to tell the difference between
    true examples
    examples we made
  use that classifier as a loss

## Slide 31: A GAN
Generative
Adversarial
Network
Grosse slides

## Slide 32
Grosse slides
Notice: we want the discriminator to make a 1 for real data, 0 for fake data
Solution (if exists, which is uncertain; and if
can be found, ditto) is known as a saddle point.
It has strong properties, but not much worth
talking about, as we don’t know if it is there or
whether we have found it.

## Slide 33
Thakar slides

## Slide 34: Important, general issue
If either generator or discriminator “wins” -> problem
Discriminator “wins”
  it may not be able to tell the generator how to fix examples
  discriminators classify, rather than supply gradient
Generator “wins”
  likely the discriminator is too stupid to be useful
Very little theory to guide on this point

## Slide 35
Grosse slides

## Slide 36
Grosse slides

## Slide 37: One must be careful about losses…
Grosse slides

## Slide 38: One must be careful about losses…
Grosse slides

## Slide 39: Alternative losses
Hinge:
  Discriminator makes D(im)
    want
      real images -> -1
      fake -> 1
  Discriminator loss:
    where y_i=-1 for real, y_i=1 for fake
  Generator loss:

## Slide 40
Dong et al 21 - Use an adversarial loss

## Slide 41: More complicated weather effects

## Slide 42: Light hits a small box of material

## Slide 43: A ray passing through scattering material

## Slide 44: More interesting…
Intensity is “created along the ray”
  by (say) airlight
  Model - the particles glow with intensity C(x)
Cross sectional area of “slab” is E
Contains particles, radius r, density rho
Too few to overlap when projected
Light out = Light in -
Light absorbed+
Light generated
Light generated: C x (area fraction
of proj. particles)
which is

## Slide 45
Shen et al 20 - Use sequence model (resnet as implicit euler method)

## Slide 47
From Lynch and Livingstone, Color and Light in Nature

## Slide 48: Raindrop scatter

## Slide 49: Backscatter
Refraction in drops causes backscatter of headlight light
  makes driving in rain at night harder
Neat trick
  (Tamburo et al 14)
  Do not illuminate raindrops by
    having headlights that are highly steerable (multiple micro mirrors)
    very fast exposure with usual illumination identifies raindrops
      too fast for driver to resolve
    now direct light between drops

## Slide 50
Tamburo et al 14

## Slide 51: Rain has multiple interesting effects
Blur from wet air
Color shifts
Puddles
Streaks
These are often quite strongly coupled to scene geometry

## Slide 52: Rain - phenomena
Drops move fast, and so create motion blur (streaks)
Garg and Nayar 07

## Slide 53: Rain - phenomena
Shallow free space - individual rain streaks
Deep free space - more bulk, fog-like effects
Hu et al 19

## Slide 54: Rain mangles detection

## Slide 55
Tremblay et al 20

## Slide 56: Simulating rain - issues
Near field:
  drops are bright, discrete, likely ballistic motion
    how bright?
    where?
    how moving?
  likely air is “wet”
    so some fogging, depending on depth
Far field:
  fog like effects
So we need to know
  depth, environment map, falling drops, camera movement

## Slide 57: Simulating rain
Tremblay et al 20

## Slide 58: Simulating rain
Trick:
  rain causes color effects, specular effects etc.
    CycleGAN is good at this, but bad at streaks
    Physics based simulation is bad at this but good at streaks
Tremblay et al 20

## Slide 59
Tremblay et al 20

## Slide 60
Tremblay et al 20

## Slide 61: Fog and rain affect LIDAR

## Slide 62: Fog and Lidar: Lidar
About 800-1000 nm
wavelength (longer than red)
Wikipedia

## Slide 63: Raindrop scatter

## Slide 64: Fog scattering
FOG

## Slide 65: What the sensor sees…

## Slide 66
Carballo, 20

## Slide 67
Fog
Rain
Very
bright
light
Carballo, 20

## Slide 68
Qualitative effects
  lost returns
  fog torus
  early returns
  rain pillars
  noise
Carballo, 20

## Slide 69
Hahner 21

## Slide 70: Radar is unaffected
Bansal et al 20

## Slide 71: Lighting affects methods, too

## Slide 72
Depth (omnimap, current best depth est)
Normal (omnimap, current best normal est)

## Slide 73: What to do?
Maybe:
  generate multiple lightings of the same image
    analogy with rain
  force method to produce same result for each
Q: How to generate multiple lightings of the same image?

## Slide 74: Hijacking knowledge
StyleGAN2 is a network that
  accepts random vectors
  produces very convincing face images (and some others; churches, etc)
  is trained by adversarial procedures
This process can be “inverted”
  GAN-inversion: given face, what random number made it?
Pretrained models like StyleGAN2 “know” a lot
  established literature around the idea that StyleGAN2 outputs are faces
    pretty much whatever you do to the input

## Slide 75: Relighting synthetic scenes
Significant literature based on “inverse graphics”
  Impute: geometry, albedo, luminaires; change luminaires; render
  Zhengqin Li thesis, 2022
  But this involves CGI,
    which we don’t trust and
    may not be available
StyleGAN Judo
  Search latent space of a generative model to find directions that
    change image
    don’t change computed albedo
  for free, resurfacing
    change image
    don’t change shading

## Slide 76: StyLitGAN Relighting

## Slide 77: Luminaire aware
Bhattad et al, 23

## Slide 78: Luminaire aware
Bhattad et al, 23

## Slide 79: StyLitGAN Resurfacing

## Slide 80: Real Images
Problem:
  who cares about normals/depth/albedo of generated images?
Idea
  apply GAN inversion to real image
  then fiddle with lighting
  THIS DOESN”T WORK
    GAN inversion doesn’t actually get you the image you started with

## Slide 81: Current GAN inverters don’t

## Slide 82: Make it so - inversion
Bhattad et al, 23

## Slide 83
Bhattad et al, 23

## Slide 84
Bhattad et al, 23

## Slide 85: Image
Bhattad et al, 23

## Slide 86: Invert
Bhattad et al, 23

## Slide 87: Relights
Bhattad et al, 23

## Slide 88: Key points
Weather effects cause detectors to work poorly
  We can collect weathered data
  OR unweather using regression procedures
  OR we can train on artificially weathered data